## Slide 1
Amakazaam! (Amazon) — stage plot
Set 9:00–9:25 pm · soundcheck 5:15 pm · contact on the day: Keira Daley
UPSTAGE (back wall)
AUDIENCE
◀ house left (stage right)
house right (stage left) ▶
DW kit · ch 1–10
Andrew (Keira on song 4)
riser 2.4 × 1.8 m
Fender · mic ch 13
Tim
Ampeg
ch 11 + 12
Vox AC30 · mic ch 15
Tyler
Vox 5 · ch 25
Tim
rhythm
guitar
Laptop · side stage, TBC
HDMI video + audio
Sam
bass
Keira's wireless · TBC
receiver out · in-ear mix in
Aaron
keys + vox
Keys (own) · stereo DI ch 19/20
Keira
lead vox
Tyler
guitar
+ vox
Vox 1 · ch 21
(over the keys)
Wireless · ch 26
straight stand
Vox 3 · ch 23
Vox 4 · fold down
Backline
Player
Vocal mic
DI box
Keys
Laptop / screen
In-ears / wireless
Dashed = not used this set
1 m · all to scale; DI boxes and mic stands slightly enlarged

## Slide 2
Amakazaam! (Amazon) — patch and notes
Set 9:00–9:25 pm · soundcheck 5:15 pm · contact on the day: Keira Daley
Ch | Input | Who and notes
1–10 | Drum kit | Andrew; Keira plays on song 4
11 | Bass DI | Sam: Ampeg DI out (uses a tuner)
12 | Bass cab mic | Ampeg cab
13 | Gtr 1 (Fender) | Tim, with pedalboard
15 | Gtr 2 (Vox AC30) | Tyler, with pedalboard
19/20 | Keys L/R | Aaron: own keyboard, stereo, needs a DI with two inputs
21 | Vox 1 | Aaron: backing on song 6. Andrew's cowbell spot on song 4
23 | Vox 3 | Tyler: co-lead on song 3, backing on song 6
25 | Vox 5 (drums) | Andrew: spoken line. Keira: sings song 4 from the kit
26 | Wireless vocal | Keira: own mic and receiver (XLR out), on a straight stand at centre
27/28 | Playback L/R | Laptop audio over HDMI: Alexa voice-over
Not used this set: ch 14, 16, 17, 18, 22, 24. Ch 31/32 are the crowd mics, for the recording only.
Monitors and in-ears
Keira has her own wireless in-ears; her transmitter takes an XLR from the desk. The mix is vocals only: her wireless (ch 26), plus Vox 5 when she sings from the kit (song 4), plus a little Vox 3 on song 3.
Screen and playback
Laptop at side stage on HDMI. Video all the way through; Alexa voice-over audio at the intro, between songs 3 → 4 and 5 → 6, and at the finish (ch 27/28). Keira runs it with a clicker.
Notes and to confirm
Song 4: Keira and Andrew swap on the kit. Andrew plays cowbell at Vox 1, then takes the kit back at the guitar solo. Where the wireless receiver and in-ear transmitter sit. Planned running time is 24:00 in a 25-minute slot.

## Slide 3
Amakazaam! (Amazon) — the set
Set 9:00–9:25 pm · soundcheck 5:15 pm · contact on the day: Keira Daley
Running time: 24:00 planned, in a 25-minute slot. The band's own run sheet has the full spoken script.
Step | Song, or what happens | Length | On stage · lead · moves | Screen · playback | Lighting
Intro | Alexa's intro (band already on stage) | 0:10 |  | Laptop audio and video | Blackout until Alexa says “Amakazaam!”, then bring up a warm wash
Song 1 | Valerie — Amy Winehouse | 3:30 | Everyone. Lead: Keira (wireless, centre) | Laptop video | Warm vintage vibes, gold and pink
1 → 2 | Straight into the next song | 0:30 | Keira talks over the intro | Laptop video | Wash with screen visible
Song 2 | Superstition — Stevie Wonder | 3:00 | Everyone. Lead: Keira | Laptop video | Groovy and spooky? Halloween orange, occasional greens, occasional disco?
2 → 3 | Straight into the next song | 0:20 | Keira talks over the intro | Laptop video | Wash with screen visible
Song 3 | Under Pressure — Queen & David Bowie | 3:30 | Everyone. Lead: Keira (wireless) and Tyler (Vox 3). Add a bit of Vox 3 to Keira's in-ears | Laptop video | Start with spotlights on lead vox (wireless) and lead guitar (Vox 3). Bright whites with red and blue accents. Build and break tension
3 → 4 | Straight into the next song, over dialogue between Keira, Alexa and Andrew | 0:30 | Andrew speaks from the kit (Vox 5), then Keira takes over the drums and Andrew moves to cowbell at Vox 1. Keira's in-ears need Vox 5 | Laptop audio and video | Wash with screen visible
Song 4 | Are You Gonna Go My Way — Lenny Kravitz | 3:00 | Everyone. Keira sings from the kit on Vox 5; Andrew on cowbell near Vox 1. At the hits at the top of the guitar solo Andrew takes the kit back, and Keira sings the final line on the wireless at centre | Laptop video | Cue: Keira's first drum fill (after the opening hits). Epic stadium: flashes on song accents, backlights, colour and movement
4 → 5 | Straight into the next song | 0:10 | Keira talks over the intro. Sam tunes down | Laptop video | Moody, but with screen visible
Song 5 | You Oughta Know — Alanis Morissette | 4:00 | Everyone. Lead: Keira | Laptop video | At the first lyric, bring the wash down to just a spotlight on lead vox. Moody blue and magenta. Start small and build to hectic
5 → 6 | Alexa dialogue | 0:10 | Keira (wireless) and Alexa (laptop). Sam tunes back up | Laptop audio and video | Wash with screen visible
Song 6 | Killing in the Name — Rage Against the Machine | 5:00 | Everyone. Lead: Keira. Backing: Tyler (Vox 3), Aaron (Vox 1) | Laptop video: the on-screen gauge explodes at the big section | Song cue: “Okay crew, we know what to do.” Start dark, end in absolute carnage: red and orange like flames, flashes on song accents, strobe by the end. Important: “destruction” lights at the big “fuck you I won't do what you tell me!” section
Finish | Alexa's outro, curtain call | 0:10 |  | Laptop audio and video | Wash with screen visible