## Slide 1
V2 Voyagers (V2 AI) — stage plot
Set 9:35–10:00 pm · soundcheck 5:00 pm · contact on the day: Holly or Shane
UPSTAGE (back wall)
AUDIENCE
◀ house left (stage right)
house right (stage left) ▶
DW kit · ch 1–10
Jai (songs 1–3) · Shane (4–5)
riser 2.4 × 1.8 m
Fender · mic ch 13
Taz
Ampeg
ch 11 + 12
Vox AC30 · not used
Laptop on the riser
HDMI video · click to drummer
Backing DI · ch 27
Taz
guitar
Cam
bass
Holly's in-ears (Xvive U4)
transmitter needs a mix feed
Acoustic DI · ch 17
Holly
lead vox
Milly
acoustic
+ vox
Vox 1 · fold down
Vox 2 · ch 22
Holly's own Beta 58
Vox 3 · fold down
Vox 4 · ch 24
Backline
Player
Vocal mic
DI box
Keys
Laptop / screen
In-ears / wireless
Dashed = not used this set
1 m · all to scale; DI boxes and mic stands slightly enlarged

## Slide 2
V2 Voyagers (V2 AI) — patch and notes
Set 9:35–10:00 pm · soundcheck 5:00 pm · contact on the day: Holly or Shane
Ch | Input | Who and notes
1–10 | Drum kit | Jai on songs 1–3 (lighter player), Shane on songs 4–5 (hard hitter)
11 | Bass DI | Cam: Ampeg DI out
12 | Bass cab mic | Ampeg cab
13 | Gtr 1 (Fender) | Taz
17 | Acoustic guitar DI | Milly
22 | Vox 2 | Holly, on her own Shure Beta 58
24 | Vox 4 | Milly: light backing vocals, and tambourine
27 | Playback L (mono) | Backing track from the band's Mooer Micro DI at the riser
Not used this set: ch 14, 15, 16, 18, 19, 20, 21, 23, 25, 26, 28. Ch 31/32 are the crowd mics, for the recording only.
Monitors and in-ears
Holly has her own wireless in-ears (Xvive U4); the transmitter needs a mix feed from the desk. The drummers' click comes from the band's own headphone amp, not the desk.
Screen and playback
The band's laptop at the drum riser runs the whole set as one Reaper session. Video over HDMI (no audio), already cut and cued, so no VJ needed. Backing track is mono, from their own Mooer Micro DI (or a house DI) into ch 27. An idle loop plays between songs.
Notes and to confirm
Two drummers; about a minute to swap before song 4. Milly chose Vox 4 (house right) but also wrote “stage right”, which is house left: confirm her side. The band asks for a smoke machine on the walk-on.

## Slide 3
V2 Voyagers (V2 AI) — the set
Set 9:35–10:00 pm · soundcheck 5:00 pm · contact on the day: Holly or Shane
Running time: 20:55 planned, in a 25-minute slot.
Step | Song, or what happens | Length | On stage · lead · moves | Screen · playback | Lighting
Walk-on | Intro video and audio | 0:30 |  | Intro audio and video | No front lighting, band in silhouette. Bring lights up as the rocket takes off. Smoke machine here too
Song 1 | Venus — Bananarama | 2:40 | Holly, Cam, Taz, Milly, Jai. Lead: Holly | Backing audio and video | Match colours of video: reds, blues, purples
1 → 2 |  | 0:15 |  | Idle loop video | 
Song 2 | Cosmic Girl — Jamiroquai | 3:40 | Holly, Cam, Taz, Milly, Jai. Lead: Holly | Backing audio and video | Match colours of video: amber, sky blue, purples
2 → 3 |  | 0:15 |  | Idle loop video | 
Song 3 | Drops of Jupiter — Train | 3:40 | Holly, Cam, Taz, Milly, Jai. Lead: Holly | Backing audio and video | Match colours of video: turquoise, deep blue, lime green
3 → 4 | Drummer changeover | 1:00 | Jai off, Shane on | Idle loop video | 
Song 4 | All Star — Smash Mouth | 3:20 | Holly, Cam, Taz, Milly, Shane. Lead: Holly | Backing audio and video | Match colours of video: deep greens, reds, sky blue
4 → 5 |  | 0:15 |  | Idle loop video | 
Song 5 | Medley: Starships — Nicki Minaj / UFO — Sneaky Sound System | 5:20 | Holly, Cam, Taz, Milly, Shane. Lead: Holly | Backing audio and video | Starships: purples, pinks, blues. UFO: golds, reds, whites